## Slide 1: BUILDING BLOCKS FOR DIFFERENT PRODUCT FORMULATIONS OF COSMETICS
Presented by:
Projyot Pravinkumar Naik
Roll no: 11
M.Pharm First Year

## Slide 2: CONTENTS:
Definition, Types, Ingredients, General formula , Manufacture & Evaluation of :-
MOISTURIZING CREAM
VINISHING CREAM
COLD CREAM
SHAMPOO
TOOTHPASTE

## Slide 3: CREAMS
Creams are defined as semisolid dosage form containing one or more drug substance dissolved or dispersed in suitable base

## Slide 4: TYPES OF SKIN CREAMS
Make up creams
  a)Vanishing cream
b)Foundation cream
2) Cleansing creams
3) Creams for winter
  a)Cold cream
4) Creams for dry skin
  a) Moisturizing cream
5) All purposes creams
6) Night creams
7) Skin protective and hand cream

## Slide 5: INGREDIENTS USED IN SKIN CREAMS
1) Water
2) Oils, fats & waxes
(a) Mineral oil (Light liquid paraffin)
(b) Glyceride oil (Almond oil)
(c) Fats (Coca butter)
(d) Waxes (Beeswax)
3) Lanolin
4) Glycol (Ethylene glycol)
5) Colours (Saffron)

## Slide 6
6) Emollients :
Also known as Moisturizers.
7) Emulsifying agents
(a) Inorganic solids (Kaolin)
(b)Gums and proteins (Gelatin)
8) Wetting agent
9) Humectants
10) Perfumes

## Slide 7: (A) MOISTURIZING CREAM
When water is lost from stratum corneum more rapidly than it is received from lower layers of skin the skin becomes dehydrated
The dehydrated skin loss its flexibility and appears rough
Creams which restore water or moisture and plasticizes the stratum corneum provides its flexibility and makes it soft these types of creams are knowns as moisturizing creams

## Slide 8
(B) VANISHING CREAM
Creams which spread easily & seem to disappear rapidly when rubbed on the skin are termed as
vanishing creams.
These creams are composed of emollient esters which leave little apparent film on the skin.
Traditional formulae of vanishing creams are based on stearic acid.
Stearic acid melts above body temperature & crystallizes in a form so as to be invisible providing a
non-greasy film .It also imparts attractive appearance to the cream.

## Slide 9: Procedure for preparation of vanishing cream :
Melt stearic acid in a china dish on a water bath.
In a beaker, dissolve potassium hydroxide in water & glycerine to it. Heat the aqueous solution upto 70°C on water bath.
When both aqueous & oily phase reaches the same temperature (70°C), add aqueous phase to melted stearic acid with constant stirring.
Remove the china dish from heat & continue the stirring, when the temperature reaches 40°C, add perfume and mix uniformly until it becomes cool and a homogeneous cream is obtained

## Slide 10: (C) COLD CREAM
Cold cream is a w/o type emulsion which when applied to skin, a cooling effect is produced, due to slow evapouration of water present in the emulsion.
Cold cream is an emulsion of fats and water which can be used to clean & soften the skin.
Cold cream has been used to remove makeup gently at the end of day & it can also be used to soften tough skin on the knees and elbows or to keep skin protected from harsh winter weather.
Cold cream is prepared by saponification reaction between beeswax & alkali borax.

## Slide 11: Procedure for preparation of cold cream : -
Weigh the required quantity of white beeswax & liquid paraffin and melt in a china dish by heating on a water bath upto 70°C.
In a glass beaker, dissolve borax in water and heat upto 70°C.
When both oily and aqueous phases reaches the same temperature (70°C), gradually add borax solution to the melted beeswax drop by drop with constant stirring.
Stir continuously until it becomes cool. When the temperature lowers to 40-45°C, incorporate rose oil and mix uniformly, until a homogeneous semi-solid mass is obtained.

## Slide 12: (D) SHAMPOO
A Shampoo is a preparation of a surfactant in a suitable form - liquid, solid or powder which when used under the specialized conditions will remove surface grease, dirt and skin debris from the hair shaft and scalp without adversely affecting the user.

## Slide 13: INGREDIENTS FOR SHAMPOO
1) Surfactants :
(a) Anionic surfactants : Alkyl benzene sulphonates
(b) Non-ionic surfactants : Fatty acid alkanolamides
(c) Amphoteric surfactants : N-alkyl aminoacids
2) Conditioning agents
lanolin
mineral oil
3) Clarifying agents
phosphates
4) Preservatives
formaldehyde
5) Perfumes

## Slide 14: Procedure for preparation of shampoo :
Measure the quantity of coconut oil, olive oil , castor oil & take it in a round bottom flask.
Potassium hydroxide dissolved in 3/4th quantity of water was added to it, heat it in a water bath for 70-80°C with constant shaking for 1hr.
Take remaining quantity of water and add sodium hexamethyl cellulose, glycerine , perfume & other ingredients.
Then mix both the solution to form a uniform shampoo.

## Slide 15: Types of Shampoo
Powder Shampoo
Lotion shampoo
Liquid shampoo
Anti-dandruff shampoo
Conditioning shampoo

## Slide 16: (E) TOOTHPASTE
Toothpaste is a paste or gel used with a toothbrush as an accessory to clean & maintain the aesthetics and health of the teeth.

## Slide 17: INGREDIENTS OF TOOTHPASTE
1) Abrasives (Calcium carbonate)
2) Detergents & oAther foaming materials (Sodium lauryl sulphate)
3) Humectants (Glycerin)
4) Binding agent (Natural gums:-Gum Arabic, gum Tragacanth)
5) Sweeting and flavouring agent (Peppermint , coriander)
6) Minor Ingredients (Titanium dioxide)

## Slide 18: Procedure for preparation of toothpaste :
Take half the quantity of water, add tragacanth powder & heat it in a water bath to get a gel.
To the remaining quantity of water, add glycerine, sodium lauryl sulphate, preservative & mix it thoroughly to get a clear solution.
Weigh the required quantity of saccharin and calcium carbonate solution & mix it with the help of mortar and pestle.
To this powder, add gum tragacanth & mix well.
Add glycerine, preservative & sodium lauryl mixture to it and triturate uniformly to get a paste.
Finally add flavouring agent & triturate well.
Transfer to a narrow mouthed plastic tube , seal & label.

## Slide 19: Thank You…..